Construction Site Visits

The lead professional service contractor and each of its subcontractors shall regularly visit the construction site during construction as part of the Construction and Review services.

A written report shall be submitted to the Department of Planning, Transport and Infrastructure (DPTI) Construction Adviser within two (2) working days of each site visit.  See Attachment 1 for proforma.

# Frequency of Visits

The exact frequency and type of inspection will be determined by the progress and nature of site activity, however as a guide the following is the minimum inspection required on small to medium size projects (up to approximately $3 million).

## Metropolitan

Professional service contractor to review Preliminaries requirements and inspect site establishment.

Professional service contractor to visit site in attendance with construction contractor at least once per week.

Subcontractors to visit site in attendance with construction contractor at least once per week at relevant stages in the construction program.

## Country (outside a 32km radius of the GPO)

Professional service contractor to review preliminaries requirements and inspect site establishment.

Professional service contractor to visit site in attendance with construction contractor at least twice per month.

Subcontractors to visit site in attendance with construction contractor at least twice per month at relevant stages in the construction program.

Projects over $3 million will require more frequent visits with some projects requiring a permanent on-site presence.  Refer to the lead professional service contract for specific services requirements.

# Inspections

## Architectural

Inspection shall be undertaken of at least:

all work to be covered up

the fixing of cladding materials

second fixings

that materials are as specified and as per sample panels.

## Civil engineering

Inspection (certified by an engineer) shall be undertaken of at least:

founding material of footings

reinforcement, footing and slab inspection

structural wall and roof framing

truss calculations (if timber truss roof)

earthworks/base

reinforced/structural concrete

drainage

pavements

backfilling material and compaction method.

## Mechanical engineering and hydraulics

Inspection shall be undertaken of at least:

air-conditioning

pipe-work in ground and walls prior to wall linings

mechanical services commissioning

under floor drainage

sewer and stormwater external and internal to building

hot and cold water at first fix

hot and cold water at second fix

sanitary fixtures second fix

backfilling material and compaction method.

## Electrical engineering and communications

Inspection shall be undertaken of at least:

first fixing prior to wall linings

on completion of 50% of fixing

commissioning.

# Contact

For more information contact:

John Callea

Manager Construction Advice

Phone:	08 8226 5315

Email:	john.callea@sa.gov.au

## Attachment 1

This document, Construction Advice Report (224) can be found in the Building Project Information Management System (BPIMS) library.

### Construction Advice and Site Visit Report

Project: Project Name

Site Address:

Contractor: Contractor Name

DPTI Project Risk Manager: Name

Phone:

Email:

| To: | Copy: | Name: | Organisation: | Email/Facsimile: |
| --- | --- | --- | --- | --- |

| Type of Inspection: |
| --- |
| Date and Time of Inspection: |
| Construction Adviser: | Date: |

| Present on Site: | Title: |
| --- | --- |

| Work in Progress: (indicate with a tick) |
| --- |
|  | Asbestos Removal |  | Concrete Construction/ Reinforcing/Formwork |  | Mechanical |
|  | Bricklaying/Stonemasonry |  | Demolition |  | Office Work Station Installation |
|  | Carpentry and Joinery |  | Electrical |  | Painting |
|  | Carpeting/Vinyl Laying |  | Fire Protection |  | Piling |
|  | Ceiling Fixing/Partitions |  | Gas Fitting/Plumbing |  | Roofing |
|  | Civil Work |  | Glazing/Aluminium Framing |  | Structural Steelwork |
|  | Cladding |  | Internal Linings |  | Tiling |
|  | Communications/Data |  | Lift, Escalators |  | Other: |

| Issues: (brief description of issues and progress.) |
| --- |
| Site Management (site area, site amenities, contamination, hazardous materials, trenching, demolition management, waste management etc) |
| Quality (documented requirements vs. completed works, materials selection, construction detailing/methodology, ESD, latent conditions) |
| Progress (achievement of milestones, anticipated final completion date, staged completion date (if applicable) for items that might be completed before the final completion date) |
| OHS&W (on site safety) |
| Communications (occupant/contractor relationships if applicable) |
| Risk Assessment (Please tick appropriate box) |
|  | High Risk |  | Medium Risk |  | Low Risk |

Other comments (Photos attached)